## Slide 1
Integridade de sinais em placas de circuito impresso
Linhas de transmissão e reflexão
Fábio Cadore Posser
Naelton Oliveira de Souza
Maio 2015

## Slide 2
TÓPICOS
Modelo de comunicação
Linhas de Transmissão
Reflexão de sinais / Ferramentas de simulação
Impedância das trilhas PCI
Técnicas de Terminação
Questões de Projeto para Controle de Impedância
Impedância Absoluta Vs. Relativa

## Slide 3
Linhas de Transmissão
  Índice de modulação:
    Am = amplitude do sinal de referência
    Ap = amplitude da portadora
Elementos Distribuídos R, L, G & C - Zo =

## Slide 4
Linhas de Transmissão
Below 1 - 2 GHz ‘R’ and ‘G’ are less significant in Digital Circuits and can be ignored.
Notice that Zo is independent of Length.
Therefore, at lower Frequencies -
Lo
Co
Zo =

## Slide 5
Linhas de Transmissão
Inner and Outer Layer Traces shown here are typical of what’s NEEDED at today’s Frequencies of Operation to achieve robust control of Transmission Lines.
(Does the Return Plane NEED to be “Ground”?)

## Slide 6
Linhas de Transmissão
When a Pulse propagates down a Transmission Line of Impedance Zo and reaches a Load of the same Impedance, ALL the energy is Transferred.
If the Downstream or Load Impedance (Zload) is different than impedance of the Line (Zo), then a percentage of the Pulse is Reflected back toward the Source.
% Reflection =
Zload - Z0
Zload + Z0
x 100

## Slide 7
Microstrip
Assumes LPI Soldermask over Bare Copper for narrow traces and thin dielectrics. Assume NO Soldermask for wide traces and Thick Dielectrics.
(NOT accurate enough for high freq analog design)

## Slide 8
Embedded Microstrip
Dimensions Must be in Inches-
i.e.- 8 mils must be expressed as .008”.
To use other units, convert 0.1
to 100 for mils
to 2.54 for mm
to .254 for cm
(NOT accurate enough for high freq analog design)

## Slide 9
Centered Stripline
(NOT accurate enough for high freq analog design)

## Slide 10
Used with Strong Drivers (Needing Incident Wave Switching).
Some Logic Families Must be Parallel Term (ECL, GTL, etc.).
Place Resistor within 1/8 Rise Distance of Last Load or just beyond Last Load.
Resistor Value = Zo.
Resistor Needed at Both Ends of Bidirectional Net.
High Power Consumption (DC Load when Output is High).
Low Power Outputs CANNOT drive this Low Impedance.
Parallel Resistor
Terminação Paralela

## Slide 11
Must place Resistor within 1/8 Rise Distance of Driver.
Resistor Value = Zo - Rs(Output Impedance).
Reflection occurs and is Absorbed back at the Driver.
Most common w/ Single Load or ALL Loads at end of Line.
Low Power Consumption.
Helps Eliminate Ground Bounce.
Lowers Power Transients and EMI Dramatically.
Series Resistor
Terminação Série

## Slide 12
12
Form of Parallel Termination with Two Resistors.
Useful w/Strong Drivers for Incident Wave Switching.
Each Resistor tied to Reference Voltage, usually Vcc & Gnd.
User Defined DC Bias, based on Resistor Values.
Parallel Combination of Resistors = Zo.
Requires Twice the Components of most Terminations.
Resistors Needed at Both Ends of Bidirectional Net.
Very High Power Consumption (Constant DC Load).
Thevinin Termination
Terminação Thévenin

## Slide 13
13
Form of Parallel Termination with Small Capacitor added.
Not Continuous Load. R to Gnd for approx 1xRC Only.
Solution for Low Power IC that Can’t have Series Term.
Resistor Value = Zo (Strong Driver) / Higher (Weak Driver).
Capacitor Value - RC = 1.5Tr (Strong Driver).
C(R+Zo) = 3Tpd (Weak Driver).
R & C Needed at Both Ends of Bidirectional Net.
Distorts the Wave of both Rising and Falling Edge.
AC or RC Termination
Terminação AC

## Slide 15
Considerações Finais
Modelo de comunicação
Linhas de Transmissão
Reflexão de sinais / Ferramentas de simulação
Impedância das trilhas PCI
Técnicas de Terminação
Questões de Projeto para Controle de Impedância
Impedância Absoluta Vs. Relativa

## Slide 16
Referências
Modelo de comunicação
Linhas de Transmissão
Exemplos de Reflexão em Sinais
Impedância das trilhas na PCI
Técnicas de Terminação
Questões de Projeto para Controle de Impedância
Impedância Absoluta Vs Relativa